## Slide 2
Introduction
Electromechanical device that converts electrical energy to mechanical energy
Mechanical energy used to e.g.
  Rotate pump impeller, fan, blower
  Drive compressors
  Lift materials

## Slide 3
How Does an Electric Motor Work?

## Slide 4
Classification of Motors
Electric Motors
Alternating Current (AC) Motors
Direct Current (DC) Motors
Synchronous
Induction
Three-Phase
Single-Phase
Self Excited
Separately Excited
Series
Shunt
Compound

## Slide 5
Field pole
  North pole and south pole
  Receive electricity to form magnetic field
Armature
  Cylinder between the poles
  Electromagnet when current goes through it
  Linked to drive shaft to drive the load
Commutator
  Overturns current direction in armature
DC Motors – Components

## Slide 6
Constant speed fixed by system frequency
DC for excitation and low starting torque: suited for low load applications
Can improve power factor: suited for high electricity use systems
Synchronous speed (Ns):
AC Motors – Synchronous motor
Ns = 120 f / P
F = supply frequency
P = number of poles

## Slide 7
Most common motors in industry
Advantages:
  Simple design
  Inexpensive
  High power to weight ratio
  Easy to maintain
  Direct connection to AC power source
AC Motors – Induction motor

## Slide 8
Components
Rotor
  Squirrel cage: conducting bars in parallel slots
  Wound rotor: 3-phase, double-layer, distributed winding
AC Motors – Induction motor
Stator
  Stampings with slots to carry 3-phase windings
  Wound for definite number of poles

## Slide 9
How induction motors work
Electricity supplied to stator
Magnetic field generated that moves around rotor
Current induced in rotor
Electromagnetics
Stator
Rotor
Rotor produces second magnetic field that opposes stator magnetic field
Rotor begins to rotate

## Slide 10
Single-phase induction motor
  One stator winding
  Single-phase power supply
  Squirrel cage rotor
  Require device to start motor
  3 to 4 HP applications
  Household appliances: fans, washing machines, dryers, mixers , wet grinders , etc.

## Slide 11
Three-phase induction motor
  Three-phase supply produces magnetic field
  Squirrel cage or wound rotor
  Self-starting
  High power capabilities
  1/3 to hundreds HP applications: pumps, compressors, conveyor belts, grinders
  70% of motors in industry!

## Slide 12
Balance single phase loads equally among three phases
Segregate single phase loads and feed them into separate line/transformer
Improve Power Quality

## Slide 13
Fixed loss
Rotor loss
Stator loss
Friction and rewinding
Stray load loss
Losses in induction motors

## Slide 14
Factors that influence efficiency
Age
Capacity
Speed
Type
Temperature
Rewinding
Load

## Slide 15
Motor part load efficiency
Designed for 50-100% load
Most efficient at 75% load
Rapid drop below 50% load

## Slide 16
  Inspect motors regularly for wear, dirt/dust
  Checking motor loads for over/under loading
  Lubricate appropriately
  Check alignment of motor and equipment
  Provide proper ventilation
Maintenance

## Slide 17
Speed Control of Induction Motor
Variable speed drives (VSDs)
Can be installed in existing system
Multi-speed motors
Wound rotor motor drives
Variable resistors to control torque performance