## Slide 1
GPS and Weapons Technology
TECHNICAL SEMINAR REPORT
ON
<number>
Notes: <number>

## Slide 2: GPS Background
<number>
The Global Positioning System (GPS) is a satellite based navigation system offering precision navigation capability. Originally designed for military use, civilian access has been permitted to specific parts of the GPS.
GPS offers a number of features making it attractive for use in aircraft navigation. Civilian users can expect a position accuracy of 100 m or better in three dimensions. The GPS signal is available 24 hours per day throughout the world and in all weather conditions. GPS offers resistance to intentional (jamming) and unintentional interference.
The equipment necessary to receive and process GPS signals is affordable and reliable and does not require atomic clocks or antenna arrays. For the GPS user, the system is passive and requires a receiver only without the requirement to transmit.

## Slide 3: Origins of GPS
First idea came after the launch of Russian Satellite Sputnik
  Two Scientists At JHU realized they could pinpoint the location of the satellite by analyzing the Doppler shift of its radio signals during a single pass.
  Frank McClure, then chairman of APL's Research Center, went a step further by suggesting that if the satellite's position were known and predictable, the Doppler shift could be used to locate a receiver on Earth; in other words, one could navigate by satellite.
GPS&WEAPON TECH
<number>

## Slide 4: Early GPS
<number>
September 1973, a system was developed combining early Navy and Air Force programs called NAVSTAR GPS
  System merged System 621B and Timation technology
    Satellites orbits were based on Timation but would have a higher altitude.
    Signal structure and frequencies were based on System 621B
    Satellites would use atomic clocks

## Slide 5: 3-Phase Development of the NAVSTAR GPS
<number>
(1974-1979)- $100 million program
  First two NAVSTAR satellites were refurbished Timation satellites carrying the first atomic clocks ever launched into space
(1978-1985)- Rockwell International
  Built a total of eleven Block I satellites launched on the Atlas-F booster.
  Design life was only 3 years but many last 10+ years
    6th Block I satellite carried a nuclear explosion detection sensor which was launched on April 36, 1980
  Block I satellites were being tested for on aircraft, helicopter, ships, trucks, jeeps, and even by men using 25-pound backpacks.

## Slide 6: 2nd Stage of GPS
<number>
Funding cut!!!- Secretary of Defense cut program by 30% ($500 million)
Result-
  Number of satellites were cut down: 24-18 (plus 3 on-orbit spares)
  Development of Block II satellites were dropped
Increased the interest in the program by stressing that GPS could increase bombing accuracy

## Slide 7: Block II Satellites
<number>
With a renew interest by the Secretary of Defense, Block II satellites were developed and launched in Feb. 1989
Operational by April 1989/created Rockwell International
  Improvements
    Full selective availability/ advanced system securities
    Improved reliability and survivability

## Slide 8: 3rd Phase
<number>
Launch of the Block II/IIA/IIR and finally IIR combining up to 33 satellites (including spares) to consist of our new GPS. GPS today uses 24 satellites and numerous ground stations
LAND
SEA
AIR
Able to get quick accurate readings no matter the weather condition, time of day, or velocity

## Slide 9: GPS Signals and Ranging
<number>
In its most basic terms, GPS determines the position of the user by triangulation. By knowing the position of the satellite and the distance from the satellite; combinations of satellites can be used to determine the exact position of the receiver.
The fundamental means for GPS to determine distance is the use of time. By using accurate time standards and by measuring changes in time, distance is computed.

## Slide 10
<number>
A simplified GPS system illustrates the concept of satellite ranging. A satellite transmits a time signal, as shown. The receiver is stationary and has an absolutely accurate clock, perfectly synchronized to GPS time. By measuring the difference in time from when the signal left the satellite to when it is received by the aircraft, the distance from the satellite to the user can be calculated. This is the product of the time difference and the speed of light (300,000 km/sec).
Notes: <number>

## Slide 11: Modern GPS
Military developed constellation of 27 satellites.
Our modern GPS primary purpose is to serve the military although, civilian users now outnumber military users.
<number>

## Slide 12: Where We Need To Go… Future Weapons Capabilities
Autonomous, Networked, Multi Role
Standoff/Long range/Persistent
Lethal / Non-Lethal (adjustable)
Mobile Targets (land and sea)
Minimize collateral damage
Quickly Integrated, Common Interfaces, Multiple-Platform carriage and release
Auto Target Recognition (ATR)
Electro-magnetic
Gun
Tactical Multi-mission
Laser Weapon
Adv Warhead
DRAAM
DROLE
Interoperability and Speed of Integration are Key
<number>
Notes: <number>

## Slide 13: Precision Weapons
Self-guiding explosives or munitions – use built-in control system and adjustable flight fins
Force multipliers that maximize efficient use of resources
Reduce unintended “collateral damage” to non-military targets
3 types: radio-controlled, laser-guided, satellite guided
Unit-27 Enhanced Guided Bomb (http://science.howstuffworks.com/smart-bomb1.htm)
<number>

## Slide 14: Remote-Controlled Weapons
Video or infrared camera relays information to plane, where remote operator steers bomb towards target
Camera keeps target in center of display – automatically directs bomb through air
Developed by U.S. and Germans in WWII, used primarily in Korea and Vietnam
GBU-15 TV/IR Bomb (http://science.howstuffworks.com/smart-bomb2.htm)
<number>

## Slide 15: Laser-Guided Weapons
Bomb equipped with a “laser seeker” sensitive to laser beam at a certain frequency
Laser “planted” on target by human operator in air or on ground
Used first in the late Vietnam War, then extensively in Desert Storm and Kosovo
Cost: approximately $60,000
GBU-10 laser-guided bomb (http://science.howstuffworks.com/smart-bomb2.htm)
<number>

## Slide 16: A Problem
Both remote-controlled weapons and laser-guided weapons rely on continued visual contact with the target. In cloudy weather, then, the bombs may veer off course, wasting the bomb and potentially causing costly damage to unintended targets.
Solution: satellite-guided weapons
<number>

## Slide 17: Satellite-Guided Weapons
The most effective and most efficient kind of precision weapons.
The bomb’s computer uses GPS signals to steer itself towards a target’s coordinates, and inertial navigation (velocity-measuring gyroscopes) if for some reason GPS fails (i.e. GPS jamming)
The most common type of satellite-guided weapon: JDAM
<number>

## Slide 18: GPS Satellites
Each of these 3,000- to 4,000-pound solar-powered satellites circles the globe at about 12,000 miles (19,300 km), making two complete rotations every day. The orbits are arranged so that at any time, anywhere on Earth, there are at least four satellites "visible" in the sky.
<number>

## Slide 19: Military GPS Applications
Cruise Missiles, Artillery, bombs, etc.
Star Wars Defense
Submarine Navigation
In the news: Captain Scott O ‘ Grady
Combating Terrorism
<number>

## Slide 20: Cruise Missiles
Cruise missile is a generic term for self-propelled guided weapons which fly like normal aircraft for much of their flight.
Almost all cruise missiles now are outfitted with GPS for navigation.
Pentagon’s favorite little toy.
<number>

## Slide 21: Tomahawks in Action
<number>

## Slide 22: Tomahawk layout
LENGTH: 5.56 meters (18ft)
WEIGHT: 1,300kg (aprox 2,200 lbs)
WING SPAN: 2.67 meters (nearly 9ft)
RANGE: 1,600km
SPEED: 880km/h (550mph)
1. Infrared imagery sensor 2. "DSMAC" guidance system 3. Data/Communications link 4. 1,000lb conventional warhead 5. "DSMAC" illuminator 6. Fuel cell 7. "TERCOM" terrain matching system 8. Turbojet subsonic engine
Source: BBC
<number>

## Slide 23: Tomahawk – Just how do they work?
Stage 1: Launch
  1 if by Land
  2 if by Sea
  3 if by Air
1
2
3
<number>

## Slide 24: Tomahawk – GPS’ Job
Cruise missiles receive an initial thrust from a detachable booster before onboard systems take over. Once airborne, it releases its wings and switches on navigational and communication systems.
The missile is guided at this early stage by GPS and onboard calculations based on its movements since launch.
<number>

## Slide 25: Tomahawk – TERCOM
TERCOM – Terrain Contour Matching
Tomahawk missiles carries a 3-D map of its route.
In theory, TERCOM allows cruise missiles to avoid detection.
<number>

## Slide 26: Tomahawk - DSMAC
DSMAC – Digital Scene Matching Area Correlation
Basically a search and destroy system
Only as good as the intelligence that the system is based on
Most accurate of all guidance systems used in cruise missiles
<number>

## Slide 27: Tomahawk – Final Destination
US military claims missiles are 90% accurate.
1,000lb warhead detonates
<number>

## Slide 28: Tomahawk – GPS’ role
This technology would be impossible without the use of GPS guiding the missile from its launch point to targets sometimes over 1000 miles away
The continuing advancement in GPS and other related technologies has dramatically decreased the cost of a standard cruise missile.
<number>

## Slide 29: Tomahawk – Future Outlook
Improved Target recognition and improved efficiency with missiles
Missile re-routing
Send live images back to base
<number>

## Slide 30: GPS and other military uses
Army is developing artillery shells that would have GPS guidance.
Pentagon allocated new resources to Excalibur artillery shells
Compared to current 155- millimeter shells, which typically land more than 370 yards from their target, Excalibur shells could hit within 10 yards of their targets and have a much greater range (more than 35 miles).
<number>

## Slide 31: Joint Direct Attack Munition (JDAM)
The most popular mechanism for delivering satellite-guided bombs, the JDAM is not an actual bomb but instead a tail kit attached to existing “dumb” bombs.
JDAM-equipped bombs have a CEP of 13m, even with a loss of GPS signal – new version accurate to 3m
Cost: approximately $18,000
<number>

## Slide 32
(http://www.fas.org)
<number>

## Slide 33: Joint Stand-Off Weapon (JSOW)
Long-range satellite-guided missile designed to hit targets from a range far beyond that of anti-aircraft weaponry
(http://www.fas.org)
<number>

## Slide 34: Potential Difficulties
GPS Jamming – this is largely accounted for by INS systems
Improving accuracy – technology limitations
Human intelligence errors (ex. Chinese Embassy mistake)
Potential terrorist capabilities (delivering biological weapons, hitting high-value targets, etc.)
Driving enemies off the conventional battlefield
Over-reliance on weapons as the way to win a war
<number>

## Slide 35: Conclusions
Precision-guided weapons, especially those equipped with GPS technology, have greatly improved the military’s strike capabilities and reduced many of the difficulties of war.
However, there are still significant improvements that can be made to maximize the efficiency of modern weapons technology.
<number>

## Slide 36: GPS and Hollywood
<number>

## Slide 37: Combating Terrorism
9/11 revisited
  The Federal Aviation Administration (FAA) is working on two GPS-based systems that would protect from hijackers
<number>

## Slide 38: THANK YOU
<number>