## Slide 1: Mechatronics

## Slide 2: Thyristors
Four layer devices
Class of semiconductor components
Wide range of devices, SCR (silicon controlled rectifier), SCS (silicon controlled switch), Diacs, Triacs, and Shockley diodes
Used in high power switching applications
i.e. hundreds of amps / thousands of watts

## Slide 3: Triacs
The Triac is a three terminal AC semiconductor switch
Turned on with a low energy signal to the Gate
MT1 and MT2 are the current carrying terminals
G is the gate terminal, used for triggering

## Slide 4: Triac Operation
5 layer device
Region between MT1 and MT2 are parallel switches (PNPN and NPNP)
Allows for positive or negative gate triggering

## Slide 5: Triac Characteristic Curve

## Slide 6: Triac Characteristic Curve
1st quadrant - MT2 is (+) with respect to MT1
VDRM is the break-over voltage of the Triac
and the highest voltage that can be blocked
IRDM is the leakage current of the Triac when VDRM is applied to MT1 and MT2
IRDM is several orders of magnitude smaller than the “on” rating

## Slide 7: Real World Triacs
Come in various shapes and sizes
Essentially all the same operationally
Different mounting schemes

## Slide 8: Triac Applications
Simple Triac Switch
Small control current/voltage
Eliminates Mechanical wear in a Relay
Much Cheaper

## Slide 9
Diodes
Overview
Brief review of semiconductors
Junction Diodes
Applications of Junction Diodes
Zener Diodes
ME 6405 – Introduction to Mechatronics 10-31-00

## Slide 10
Diodes
ME 6405 – Introduction to Mechatronics 10-31-00
Review of Semiconductors
The two semiconductors of greatest importance are Silicon (Si) and Germanium (Ge)
Both elements have four valence electrons
The conduction band is defined as the lowest unfilled energy band
The valence band is an energy region where the states are filled or partially filled by valence electrons
Electrons in the valence band can be moved to the conduction band with the application of energy, usually thermal energy

## Slide 11
A material can be classified as: 1. Insulator – has valence and conduction bands well separated 2. Semiconductor – has valence band close to conduction band (the energy gap is about 1eV). 3. Conductor – has the conduction and valence bands overlapping
Pure semiconductors (Si, Ge) are poor conductors
Semiconductors are valuable for two unusual properties:
1. Conductivity increases exponentially with temperature (ex: Thermistor)
2. Conductivity can be increased and precisely controlled by adding small impurities in a process called doping.
ME 6405 – Introduction to Mechatronics 10-31-00

## Slide 12
n-type doping – adds impurities from column V of the periodic table to a semiconductor material. Negative free charge carriers (electrons) become available.
p-type doping – adds impurities from column III of the periodic table to a semiconductor material. Positive free charge carriers (holes) become available.
A diode is created when a p-type semiconductor is joined with and n-type semiconductor by the addition of thermal energy.
When both materials are joined, the thermal energy causes positive carriers in the p-type material to diffuse into the n-type region and negative carriers in the n-type material to diffuse into the p-type region.
This creates the depletion region within the diode.
ME 6405 – Introduction to Mechatronics 10-31-00

## Slide 13
n
p
Depletion Region
Mayority carriers
Mayority carriers
The depletion region contains an internal electric field caused by the separation of charge. This is called the potential barrier and it acts to oppose the diffusion of majority carriers across the junction.
Under open circuit conditions no current flows through the diode.
ME 6405 – Introduction to Mechatronics 10-31-00

## Slide 14
Current flow in the diode
The behavior of a diode depends on the the polarity of the circuit
A diode is forward biased if the positive terminal of the battery is connected to the p-type material. The majority carriers are forced towards the junction and the depletion region decreases.
If the voltage is high enough the depletion region can be entirely eliminated.
Current is sustained by the majority carriers.
ME 6405 – Introduction to Mechatronics 10-31-00
Forward Biased
n
p
if
Depletion Region
Original Size
Vo
Vo-V
V
Potential Barrier

## Slide 15
Current flow in the diode
A diode is reverse biased if the positive terminal of the battery is connected to the n-type material. The majority carriers are forced away from the junction and the depletion region increases.
The majority carriers are unable to create a current
There is a small reverse current or leakage current sustained by the minority carriers
If reverse bias is sufficiently increased, a sudden increase in reverse current is observed. This is known as the Zener or Avalanche effect
ME 6405 – Introduction to Mechatronics 10-31-00
n
p
Reverse Biased
Depletion Region
Original Size
ir
Vo
Vo+V
V
Potential Barrier

## Slide 16
V
I
conduction
region
non-conduction
region
Ideal Curve
Diode characteristic curve
ME 6405 – Introduction to Mechatronics 10-31-00
Ideal Diode – no resistance to current flow in the forward direction and infinite resistance in the reverse direction. (Equivalent to a
switch).

## Slide 17
Diode Specifications
ME 6405 – Introduction to Mechatronics 10-31-00
Forward Voltage Drop (Vf) - specified at the forward current (if). Typically 0.3 V for Germanium and 0.7 V for Silicon.
Leakage Current – specified at a voltage less than the breakdown voltage. Leakage current is undesirable and will be present until the breakdown voltage is reached. Junction diodes are intended to operate below their breakdown voltage.
Current Rating – determined primarily by the size of the diode chip, material used, and configuration of the package. Average current is used (not RMS current).

## Slide 18
Diode Specifications
ME 6405 – Introduction to Mechatronics 10-31-00
Minimum Diode Specifications
- Maximum reverse voltage - Max. reverse voltage that will not cause breakdown
- Rated forward current – Max. amount of average current permitted to flow in forward direction
- Maximum forward voltage drop – Max. forward voltage drop across diode @ indicated
- Maximum leakage current -
- Maximum reverse recovery time
Switching - The switching speed of a diode depends upon its
construction and fabrication. - Generally, the smaller the chip the faster it switches (other things being equal).
- The reverse recovery time, trr , is usually the limiting parameter (trr is the time it takes a diode to switch from ON to OFF).
current

## Slide 19
Diode Applications
ME 6405 – Introduction to Mechatronics 10-31-00
Half-wave rectifier circuit
Full-wave rectifier circuit
R
R
- Rectified signal is a combination of an AC signal and a DC component ( known as a DC pulse)
- The diodes act to route the current From both halves of the AC wave

## Slide 20: Zener Diode
Zener diodes operate in the breakdown region.
Zener diodes have a specified voltage drop when they are used in reverse bias.
Every pn junction (i.e. diode) will break down in reverse bias if enough voltage is applied.
Zener diodes are operated in reverse bias for normal voltage regulation.
Able to maintain a nearly constant voltage under conditions of widely varying current.
Notes: <number>
10/31/00 ME 6405: Introduction to Mechatronics<number>

## Slide 21: Zener Diode I-V Graph
Zener characteristics and parameters
Notice that as the reverse voltage VR is increased, the leakage current remains essentially constant until the breakdown voltage VZ (Zener voltage).

## Slide 22: Types of Breakdowns
Zener breakdown - the electric field near the junction becomes large enough to excite valence electrons directly into the conduction band.
Avalanche breakdown –minority carriers are accelerated in the electric field near the junction to sufficient energies that they can excite valence electrons through collisions.
Note: The predominance of one breakdown over the other depends on the room temperature.

## Slide 23: Zener Diode Applications
Can serve as a “Voltage Regulator” when placed in parallel across a load to be regulated.

## Slide 24: Zener Diode Specifications
Basic Parameters
  Zener Voltage (VZ) – common range, 3.3 V to 75 V
  Tolerance of Zener Voltage – commonly 5 to 10%
  Test current (IZ) – correspondent to Vz
  Power handling capability – ¼, ½, 1, 5, 10, 50 W

## Slide 25: Thermistor
Thermistor - Temperature sensitive resistor
Their change in electrical resistance is very large and precise when subjected to a change in temperature.
Thermistors exhibit larger parameter change with temperature than thermocouples and RTD’s.
  Thermistor - sensitive
  Thermocouple - versatile
  RTD – stable
Generally composed of semiconductor materials.
Very fragile and are susceptible to permanent decalibration.

## Slide 26: Thermistor Probe
TEFLON INSULATION
TEFLON TUBE
2” MIN.
.095” DIA. MAX.
.11 DIA. MAX.
#32 TINNED COPPER WIRE 3” LONG
One of many available probe assemblies

## Slide 27: Thermistor Characteristics
Most thermistors have a negative temperature coefficient (NTC); that is, their resistance decreases with increasing temperature.
Positive temperature coefficient (PTC) thermistors also exist with directly proportional R vs. T.
Extremely non-linear devices (high sensitivity)
Common temperature ranges are –100 oF (~-75 oC) to +300 oF (~150 oC)
Some can reach up to 600 oF

## Slide 28: Thermistor R-T Curve
An individual thermistor curve can be very closely approximated by using the Steinhart-Hart equation:
=
T = Degrees Kelvin
R = Resistance of the thermistor
A,B,C = Curve-fitting constants
Typical Graph
Thermistor (sensible)
RTD (stable)
Thermocouple (versatile)
T
V or R

## Slide 29: Thermistor Applications
Temperature Measurement
  “Wheatstone bridge” with selector switch to measure temperature at several locations

## Slide 30: Thermistor Applications
Resistor is set to a desired temperature (bridge unbalance occurs)
Unbalance is fed into an amplifier, which actuates a relay to provide a source of heat or cold.
When the thermistor senses the desired temperature, the bridge is balanced, opening the relay and turning off the heat or cold.
Temperature Control
high gain amplifier
relay
thermistor
variable resistor for setting desired temperature

## Slide 31: Phototransistor Background
Operation similar to traditional transistors
Have a collector, emitter, and base
Phototransistor base is a light-sensitive collector-base junction
Small collector to emitter leakage current when transistor is switched off, called collector dark current

## Slide 32: Phototransistor Package types

## Slide 33: Phototransistor Construction

## Slide 34: Phototransistor Operation
A light sensitive collector base p-n junction controls current flow between the emitter and collector
As light intensity increases, resistance decreases, creating more emitter-base current
The small base current controls the larger emitter-collector current
Collector current depends on the light intensity and the DC current gain of the phototransistor.

## Slide 35: Basic Phototransistor Circuit
The phototransistor must be properly biased

## Slide 36: Obstacle Avoidance Example

## Slide 37: Obstacle Avoidance Example
Adjust baffle length to obtain a specific detection range
Use infrared components that won’t be affected by visible light
Use ~ 220 ohm resistors for LED’s
Use multiple sensors in a row to detect narrow obstacles

## Slide 38: Phototransistor Summary
They must be properly biased
They are sensitive to temperature changes
They must be protected against moisture
Hermetic packages are more tolerant of severe environments than plastic ones
Plastic packages are less expensive than hermetic packages

## Slide 39: Optoisolator Background
Operation similar to relays
Used to control high voltage devices
Excellent noise isolation because switching circuits are electrically isolated
Coupling of two systems with transmission of photons eliminates the need for a common ground

## Slide 40: Optoisolator Construction
Glass dielectric sandwich separates input from output

## Slide 41: Optoisolator Schematic
Input Stage = infrared emitting diode (IRED)
Output Stage = silicon NPN phototransistor

## Slide 42: Optocoupler Interrupter Example
Similar to lab setup
Used to calculate speed or distance
Integrated emitter and detector pair
Easy to install

## Slide 43: Optocoupler Interrupter Schematic
Eliminates mechanical positioning problems encountered in adjusting the emitter and detector for proper sensing

## Slide 44: Optoisolator Summary
Ideal for for applications requiring
  High isolation surge voltage
  Noise isolation
  Small size
Signal cannot travel in opposite direction
Used to control motors, solenoids, etc.