## Slide 1: PLANER MILLING MACHINE ACCOMMODATED WITH DRILL-HEAD
Mini project report on

## Slide 2: INTRODUCTION:
What is Planer-milling machine?
Planers and shapers are now obsolescent, because milling machines have eclipsed them as the machine tools of choice for doing work, as the rate of metal removal is quantitative.

## Slide 3
planer-milling machines come in two kinds: double-housing and open-side. The double-housing variety has vertical supports on both sides of its long bed; the open-side variety has a vertical support on only one side, allowing the work piece to extend beyond the bed.

## Slide 4: Planer milling machine (PMM)

## Slide 5: MACHINE CONFIGURATION
Surface area of work table:
4 metres * 6 metres.
Maximum distance between the work table & the arm:
2 metres.
Maximum weight of work that the bed can withstand:
45 tones.

## Slide 6: SETUP OF WORK PIECE ON THE MACHINE
Lift the work piece, using hoist, to position on machine bed.
Secure work piece in holding fixture, using wrenches, and verify position, using gauges, calipers, or square.
Select cutting tool and mount it in spindle, using hand tools. Adjust controls to set feed rate, speed of cutting tool, and depth of cut.
start machine, and engage automatic feed. Observe operation, stop machine to change cutting tool, and adjust controls.

## Slide 7: LEVELING OF WORK TABLE USING LONG FLEXIBLE LIQUID COLUMN
Leveling of work table or machine bed, using a long flexible liquid column is a simple technique.
leveling of work tables having configuration about 6 mts * 4 mts, is difficult and not secure, with spirit levels or any other techniques.

## Slide 8: WHEN TABLE IS LEVELED IMPROPERLY

## Slide 9: WHEN THE TABLE IS PROPERLY LEVELED

## Slide 10: ADVANTAGES
Skilled workers are not necessary for leveling the table.
Maintenance is simple
Very cheap
Lengthier and wider work tables can also be leveled with less effort.
Work setup time is reduced.

## Slide 11: PMM ACCOMMODATED WITH DRILL HEAD
It is not easy to change over the work parts weighing about and more than 15 tones from one machine to other.
Here in our conversation it is assault on time and power if the work part is to be transferred from milling machine to drilling machine for the purpose of drilling.
So the innovation of the project is that, drilling head is to be attached to the lead screw of the arm through half-nut arrangement.

## Slide 12: DRILL HEAD

## Slide 13: BENEFITS
Drilling and planer surface machining with mill tool are accommodated on the single unit.
Work transfer time and lead time are decreased to maximum level.
More power is saved, as there is no transfer of tones from one machine to another.
Overall production is increased.

## Slide 14: CONCLUSION
Using these types of combined manufacturing units as one stations in production system, there is increase in production, and there by decrease in pricing, shop floor area, work changing time, power etc.